## Slide 1: Computer system overview
BASIC ELEMENTS OF A COMPUTER:
Processor- controls operations & performs data processing..
main memory – volatile, used by processor for currently running appliications
i/o modules – move data to& from computer & i/o devices
System bus – communication among processors, RAM, & i/o modules
2 internal registers used by processor:----------
MAR ( memory address register) : stores addresss of next read/write operations
MBR ( memory buffer register): STORES the data to be read from or written into memory
I/OAR( input output address register): specifies a particular input output
I/OBR : exchange of info. bw i/o module & processor.
SOME DEFINITIONS:---------------------------------------------------
Memory module: set of sequentially numbered memory locations
i/o module: transfers data from i/o devices to processor & memory & vice versa.

## Slide 2: PROCESSOR REGISTERS
1. USER VISIBLE REGISTERS:( used in place of RAM for faster access time)
2. Control & status registers( used to control operations of processor & execution of programs)
USER VISIBLE REGISTERS:
May be referenced by means of the machine language `
DATA REGISTERS: general purpose registers asssigned to functions by programmer
ADDRESS REGISTERS: contains address of data and instructions in RAM. Maybe be general Purpose or dedicated.
i) INDEX REGISTER- adding index to a base address to get effecctive address.
ii) SEGMENT REGISTER – memory is divided into segments….
iii) STACK POINTER
CONTROL & STATUS REGISTERS( control the opertations of the processor, not visible to user generally)
PROGRAM COUNTER: contains address of next instructions to be fetched
INSTRUCTION REGISTER: contains currently executing instruction.

## Slide 3: INSTRUCTION EXECUTION
Instruction processing consists of 2 steps:
1. fetching instructionns from memory (FETCH STAGE)
2. executioning each instructions ( EXECUTE STAGE)
The processing required for each instructions is called instruction cycle
4 STEPS DURING INSTRUCTION PROCESSSING: ---------------------
1. processor- memory
2. processor- I/O
3. data processing
4. control

## Slide 4: INTERRUPTS
All computers provide a mechanism by which other modules (I/O , memory) may interrupt the normal execution of processor.
Basically done for improving processor utilization.
CLASS OF INTERRUPTS: ---------------------
1.program
2. timer
3. I/O
4. hardware failure

## Slide 5: Multiprogramming
Multiprogramming is a rudimentary form of parallel processing in which several programs are run at the same time on a uniprocessor. Since there is only one processor, there can be no true simultaneous execution of different programs.

## Slide 6: CACHE MEMORY
It is invisible to OS.
Interacts with the other memory management hardware.
cache memory, also called cache, supplementary memory system that temporarily stores frequently used instructions and data for quicker processing by the central processing unit (CPU) of a computer. The cache augments, and is an extension of, a computer's main memory.

## Slide 7: I/O COMMUNCIATION TECHNIQUES
Programmed I/O
Interrupt-driven I/O
DIRECT MEMORY ACCESS ( DMA)